## Slide 1
HackHardware · Getting started with the ESP32
1
Getting started with the ESP32
A two-hour hands-on workshop. You leave with a board that serves a web page to your phone.
HackHardware
[DATE] · [ROOM]
Code and notes: github.com/galileoisonline/esp32-workshop
Notes: Welcome. This is a hands-on session: about twenty minutes of me talking, then five short tasks you do on your own board, with breaks in between where I explain what just happened.
You do not need any electronics background. If you can install a program and edit a line of text, you can do everything today. Helpers are the people with [stickers / name tags]; if you are stuck for more than two minutes, wave.
While I go through the first slides, keep installing the software from the setup guide if you have not finished. The link on the slide has the setup guide, all the code, and a troubleshooting page.

## Slide 2
HackHardware · Getting started with the ESP32
2
Plan for the next two hours
Time | What | You
0:00 | Setup check: IDE installed, board shows up as a serial port | install, plug in
0:10 | How the ESP32 works: the parts you need to know before writing code | listen, ask
0:30 | Task 1 · Blink an LED | first upload
0:45 | Task 2 · Serial output and a button | read inputs, print
1:00 | Short break | 
1:05 | Task 3 · Turn on Wi-Fi | scan, start a network
1:20 | Task 4 · A web page served by the board | control it from a phone
1:45 | Task 5 · Board-to-board messages (optional) or a challenge of your choice | build
2:00 | Wrap-up: show what you built, where to go next | 5 min
Each task is a complete, working sketch in the repo. If you fall behind, open the next one. Nothing depends on you having finished the previous task.
Notes: Here is the plan. The first twenty minutes are background: what is actually on the board, how the code gets onto it, and what is running underneath your program. I am going deeper than a typical intro because these are the things that explain the errors you will hit later.
Then five tasks of about fifteen minutes each. Every task has one thing you can see that tells you it worked: an LED, a line of text, a Wi-Fi network on your phone. When you see it, you are done and can try the extras.
Every task is a complete sketch that works as-is. If you fall behind, open the next one; you will not miss anything that later tasks depend on.

## Slide 3
HackHardware · Getting started with the ESP32
3
Before we start: setup check
1. Install Arduino IDE 2.x (2.3.10 or newer).
2. File → Preferences → Additional boards manager URLs, paste: https://espressif.github.io/arduino-esp32/package_esp32_index.json
3. Boards Manager, search *esp32*, install esp32 by Espressif Systems (3.3.x, about 300 MB; this is normal).
4. Tools → Board → esp32 → ESP32S3 Dev Module. Leave the other Tools entries at their defaults.
5. Plug a USB-C data cable into the connector labelled UART (not the one labelled USB). Tools → Port should show a new entry.
6. Download the repo ZIP from github.com/galileoisonline/esp32-workshop and unzip it.
What the port looks like
macOS | /dev/cu.usbserial-0001 or /dev/cu.SLAB_USBtoUART
Windows | COM3, COM5 …
Linux | /dev/ttyUSB0 (add yourself to the dialout group)
No port? It is nearly always the cable; many USB-C cables carry power only. Port appears but you will see no Serial output later? You are on the wrong connector: move to UART. Ask a helper now, not during Task 1.
Notes: Before anything else, we need the toolchain working on your laptop. Arduino IDE 2, then the ESP32 board package from Espressif. The URL goes into Preferences under Additional boards manager URLs; after that, Boards Manager lets you install "esp32 by Espressif Systems". It downloads about three hundred megabytes of compilers and libraries, so it takes a few minutes. That is normal.
Then select the board: ESP32S3 Dev Module. Your board has two USB-C connectors, labelled UART and USB on the silkscreen. Use UART. That one goes through a USB-to-serial chip, shows up as a normal port, and everything in the IDE just works. The USB one is the chip's own USB port: uploads work through it too, but the Serial Monitor stays empty unless you change a setting, and that confuses everyone. Under Tools, Port, you should see a new entry, usbserial or SLAB on a Mac, COM-something on Windows.
The number one problem at this point is the cable. A lot of USB cables are charge-only and have no data wires. The board lights up but nothing appears under Port. Second most common is a missing driver for the serial chip. Both are five-minute fixes if you raise your hand now, and a twenty-minute delay if you wait until Task 1.

## Slide 4
HackHardware · Getting started with the ESP32
4
What a microcontroller is
 | Your laptop | ESP32 dev board
Processor | 4–12 cores at 3–5 GHz | 2 cores at 240 MHz
Memory | 8–32 GB RAM | 512 KB SRAM (+ 8 MB PSRAM on this board)
Storage | 512 GB SSD | 8 MB flash (holds your program)
Operating system | macOS / Windows / Linux, many processes | None you interact with. One program, started at power-on, runs until power is removed.
Talks to | screen, keyboard, disk, network | pins: 3.3 V on or off, voltages, pulses. Plus Wi-Fi and Bluetooth.
Boot time | 10–30 s | about 300 ms
Power | 15–60 W | 0.3 W active, 25 µW asleep
Price | $1000+ | $4–15
The point is not that it is small. It is that it is deterministic and directly wired to the physical world: your code decides what a pin does, and nothing else is competing for the processor.
Notes: A microcontroller is a full computer on one chip: processor, memory, storage, all the peripherals. The numbers look tiny next to a laptop, but the difference in kind matters more than the difference in size.
There is no operating system in the sense you are used to. There is a small real-time scheduler underneath, which we will get to, but you do not log in, there are no apps, nothing else is running. Your program starts about three hundred milliseconds after power arrives and runs until power is removed. Unplug it, plug it back in, same program starts again.
And instead of a screen and keyboard, it talks to pins. A pin is a wire you control from code: put three point three volts on it, or read the voltage that is on it. LEDs, buttons, sensors, motors all reduce to that. The ESP32 adds a Wi-Fi and Bluetooth radio on the same chip, which is the reason it is so popular.

## Slide 5
HackHardware · Getting started with the ESP32
5
What is inside the chip
Block | ESP32-S3 (on your board)
CPU | 2 × Xtensa LX7, 32-bit, up to 240 MHz, vector instructions
SRAM | 512 KB (about 300 KB free once Wi-Fi is up)
PSRAM | 8 MB in the module (R8 variants): images, audio, big buffers
ROM / RTC RAM | 384 KB bootloader ROM · 16 KB RTC memory that survives deep sleep
Flash | 8 or 16 MB in the module, executed in place through a cache
Radio | Wi-Fi 802.11 b/g/n, 2.4 GHz only · Bluetooth 5 LE (no Bluetooth Classic)
USB | native USB OTG: serial, JTAG debugging, or act as a keyboard
Digital I/O | 45 GPIO pins (not all usable; see the next slides)
Analog | 2 × 12-bit ADC, 20 channels · no DAC
Other | 14 capacitive touch pads, temperature sensor
Peripherals | 3 UART, 2 I²C, 4 SPI, 2 I²S, TWAI (CAN), 8 PWM channels, RMT, LCD/camera, SD/MMC
The original ESP32 (2016) is the cheaper sibling in most tutorials: LX6 cores, Bluetooth Classic, 34 GPIO, no native USB. Today's code runs on it with three lines changed in config.h. ESP32-C3 / C6 are the small RISC-V ones.
Arduino for ESP32 is a layer on top of Espressif's own framework, ESP-IDF 5.5. Every Arduino call ends in an ESP-IDF call; you can mix them freely.
Notes: This is the block list for the chip on your board, the ESP32-S3. Two 32-bit Xtensa LX7 cores at up to 240 megahertz, with vector instructions that make it usable for small neural networks, which is why it shows up in camera and voice products. Half a megabyte of SRAM on the chip, of which your program gets roughly 300 kilobytes once the Wi-Fi stack has taken its share, plus eight megabytes of PSRAM in the module on the R8 variant for big buffers. The program itself lives in an eight or sixteen megabyte flash chip inside the module and is executed straight from there through a cache.
Then the reason people buy it: a 2.4 gigahertz Wi-Fi radio and Bluetooth Low Energy on the same die. Note it is LE only; the original ESP32 also did Bluetooth Classic, the S3 does not. And a native USB port, which the original did not have: it can be a serial device, a debugger, or pretend to be a keyboard.
Peripherals: 45 general purpose pins, two analog to digital converters, fourteen touch pads, PWM on eight channels, all the usual serial buses, plus interfaces for cameras and displays. We will use the touch pads and the internal temperature sensor today because they need no extra parts.
Two notes. The original ESP32 is what most tutorials online use; the code today runs on it with three lines changed. And Arduino on ESP32 is not a separate world: it is a thin layer on Espressif's own framework, ESP-IDF version 5.5. When you outgrow Arduino you keep everything you learned.

## Slide 6
HackHardware · Getting started with the ESP32
6
Chip, module, board
Development board ESP32-S3-DevKitC-1 (what you hold)
two USB-C connectors (UART via a CP2102N chip, and native USB) · 3.3 V regulator · RST and BOOT buttons · RGB LED · 44 header pins
Module ESP32-S3-WROOM-1 (N8R8, N16R8 …)
PCB antenna · 8 or 16 MB flash · 8 MB PSRAM on R8 variants · 40 MHz crystal · metal shield
Chip ESP32-S3
2 × Xtensa LX7 @ 240 MHz · 512 KB SRAM · 384 KB ROM · Wi-Fi and Bluetooth LE radio · USB OTG · GPIO, ADC, touch, PWM, UART, I²C, SPI, I²S, TWAI
When someone says “an ESP32” they may mean any of the three. What you buy for a project is a module (certified radio, flash, antenna). What you buy to learn is a board.
Notes: Three words that get used interchangeably. The chip is the silicon. On its own it is useless to us: it needs a crystal, flash memory, an antenna, and radio certification. Espressif sells all that soldered together under a metal shield as a module; on your board it is the ESP32-S3-WROOM-1, the rectangular can. The suffix, N8R8 or N16R8, means eight or sixteen megabytes of flash and eight of PSRAM. If you ever design your own circuit board, you buy the module, not the chip.
A development board wraps the module with everything you need to program it from a laptop: USB connectors, a USB-to-serial converter chip, a voltage regulator that turns USB's five volts into the three point three the chip needs, a reset button, a button on GPIO 0, an LED, and pin headers so you can plug wires in.
Hold your board and find the module and the small USB-to-serial chip between the two USB-C connectors. That chip is what shows up as the port on your laptop when you use the UART connector. The other connector goes straight into the chip's own USB port.

## Slide 7
HackHardware · Getting started with the ESP32
7
Board tour: ESP32-S3-DevKitC-1
antenna
ESP32-S3-WROOM-1
module (N8R8: 8 MB flash, 8 MB PSRAM)
3V3
3V3
RST
4 touch T4
5
6
7
15
16
17
18
8 I²C SDA
3 strapping
46 strapping
9 I²C SCL
10 SPI SS
11 SPI MOSI
12 SPI SCK
13 SPI MISO
14
5V in
GND
GND
TX Serial
RX Serial
1
2
42
41
40
39
38 RGB LED (v1.1)
37 PSRAM
36 PSRAM
35 PSRAM
0 BOOT
45 strapping
48 RGB LED (v1.0)
47
21
20 USB D+
19 USB D-
GND
GND
RGB LED GPIO 48 or 38
RST
BOOT
→ GPIO 0
CP2102N
USB–UART
USB-C UART
USB-C USB
use this one
native USB / JTAG
– Two USB-C connectors. UART goes through the CP2102N serial chip: use it. USB is the chip's native USB: uploads work, Serial output does not appear unless you enable *USB CDC On Boot*.
– RST resets the chip. BOOT connects GPIO 0 to ground.
– The LED is an addressable RGB LED (WS2812 type) on one data pin: GPIO 48 on the original board, GPIO 38 on v1.1. Both are in circulation and look identical. The red LED next to the connectors is power.
– 3V3 and GND power external parts. 5V is the USB input.
– All pins are 3.3 V logic. 5 V on an input can damage the chip.
– A pin sources about 12 mA by default (up to 40 mA configured): an LED with a resistor, not a motor.
– Trust the GPIO number printed on the board, not the position.
Notes: This is the ESP32-S3-DevKitC-1, Espressif's own board for this chip. Forty-four pins, two USB-C connectors, two buttons, one LED.
The module is in the middle, with the antenna at the top edge. Keep your fingers off the antenna when testing Wi-Fi range. At the bottom, two USB-C connectors, labelled on the board. The one labelled UART goes through a CP2102N serial chip, and that is the one we use all day. The one labelled USB goes straight into the chip; it is great for debugging later, but with the default IDE settings the Serial Monitor stays empty on it, and people spend twenty minutes wondering why. If your board shows up as usbmodem on a Mac, you are on the wrong one.
Two buttons: RST resets the chip, BOOT connects GPIO 0 to ground. We use BOOT as an ordinary input in Task 2 and to force programming mode when uploads fail.
The LED is not a plain LED. It is an addressable RGB LED, the same kind as in LED strips, driven by a single data pin. On the original board that pin is 48, on the v1.1 revision it is 38, and you cannot tell which you have by looking. Our config.h says 48; if nothing lights up in Task 1, change it to 38. The red LED near the connectors is just power.
Voltages: everything is 3.3 volts. 3V3 is a regulated output you can power sensors from; 5V is the USB input. Never put five volts on a GPIO pin. A pin drives about twelve milliamps, which is an LED, not a motor.

## Slide 8
HackHardware · Getting started with the ESP32
8
Which pins you can actually use
GPIO | Restriction | Why
26–32 | Never use | Wired to the flash inside the module. Not on the headers, but you will see them in code.
35, 36, 37 | Avoid on R8 / N16R8 boards | Used by the 8 MB octal PSRAM. They are on the header; driving them corrupts memory.
0, 3, 45, 46 | Strapping pins: careful at boot | Sampled at reset. 0 low = download mode (that is BOOT). 45 high = 1.8 V flash setting → will not boot. 46 must be low. Usable after boot.
19, 20 | USB D− / D+ | The second USB-C connector and the built-in debugger live here. Leave them alone.
43, 44 | TX0 / RX0 | This is Serial, via the UART connector. Using them for anything else kills your Serial Monitor.
38 or 48 | RGB LED | Whichever your board revision uses. The other one is free.
11–20 | ADC2: unreliable while Wi-Fi is on | ADC2 is shared with the radio driver. For analogRead use ADC1 = GPIO 1–10.
1, 2, 4–18, 21, 39–42, 47 | Free for outputs and inputs | The list to reach for. 8/9 are the default I²C pins, 10–13 the default SPI pins, 1–14 are the touch pads T1–T14. No input-only pins on this chip.
Source: ESP32-S3 datasheet and hardware design guidelines, ESP32-S3-DevKitC-1 user guide. This table is on the cheat sheet in the repo.
Notes: This is the slide that will save you the most time later, so it is worth two minutes. Not every pin with a number on it is free.
Twenty-six to thirty-two are the flash bus inside the module; they are not on your headers, but you will see the numbers in code and error messages. Thirty-five, thirty-six and thirty-seven are on the header, but on boards with eight megabytes of PSRAM, which is what most DevKitC-1s are, they are the PSRAM bus. Drive them and memory gets corrupted in interesting ways. Avoid them.
Zero, three, forty-five and forty-six are strapping pins. The chip reads them at the instant of reset to decide how to boot; once running they are ordinary pins, which is why the BOOT button can sit on GPIO 0. But wire something that holds forty-five high at reset and the chip configures its flash for one point eight volts and never boots. People lose afternoons to that.
Nineteen and twenty are the USB data lines for the second connector. Forty-three and forty-four are your serial console. Thirty-eight or forty-eight is the LED.
The ADC2 note: the second analog converter is shared with the Wi-Fi driver, so analog reads on pins eleven to twenty are unreliable once Wi-Fi is on. Use one to ten for analog.
The last row is the list to reach for. It is on the cheat sheet. One nice thing about this chip compared with the original ESP32: there are no input-only pins, every pin can do both and has pull-up resistors.

## Slide 9
HackHardware · Getting started with the ESP32
9
Power: what the board draws and why uploads fail on hubs
Mode | What is on | Current (chip only)
Active, Wi-Fi transmitting | CPU + radio TX | peaks of 280–340 mA
Active, Wi-Fi idle / receiving | CPU + radio RX | about 90 mA
Active, radio off | CPU only, 240 MHz | 40–60 mA
Modem-sleep, 40 MHz | CPU idle, radio off | 13–20 mA
Light-sleep | CPU paused, RTC on | 240 µA (+140 µA with PSRAM)
Deep-sleep | RTC + 16 KB RTC memory only | 7–8 µA
Power off | CHIP_PU low | 1 µA
ESP32-S3 datasheet figures. A dev board adds 5–20 mA for its regulator, power LED and serial chip, so a board never reaches 8 µA without modification.
– USB gives 5 V. A linear regulator (SGM2212 on this board) drops it to 3.3 V and wastes the difference as heat.
– Wi-Fi TX draws short spikes near 300 mA. A weak USB port, a long thin cable or an unpowered hub sags below ~2.8 V and the chip resets: Brownout detector was triggered
– Fix: a direct port on the laptop, a short cable, or a powered hub. Not a code problem.
– Deep sleep is how battery projects run for months: wake on a timer or a touch pin, do a few hundred ms of work, sleep again. RTC memory keeps a few variables across sleeps.
Notes: If you are behind schedule, this slide can be skipped; the same content is in docs/CHEATSHEET.md.
A quick word about power, because it explains one of the most confusing errors you can hit. The chip runs at three point three volts, and the board makes that from USB's five volts with a simple linear regulator.
When Wi-Fi transmits, the current draw spikes past three hundred milliamps for a few milliseconds. A weak USB port, an unpowered hub, or one of those very thin cables cannot deliver that, the voltage sags, and the chip's brownout detector resets it. In the Serial Monitor you see "Brownout detector was triggered" and the board reboots in a loop. It looks like a software bug. It is a power problem: plug straight into the laptop with a short cable.
The rest of the table is why people use this chip for battery projects. Active it draws tens of milliamps. In deep sleep, with only the real-time clock running, seven or eight microamps. Sixteen kilobytes of RTC memory survive that sleep, so a sensor can wake every ten minutes, take a reading, send it, and go back to sleep for months on a couple of AA cells. We will not do that today, but it is in the challenges.

## Slide 10
HackHardware · Getting started with the ESP32
10
How your code gets onto the chip
your .ino
+ Arduino core
+ ESP-IDF
xtensa-esp-elf-gcc
firmware.bin
esptool.py
SPI flash
on the module
reset
ROM bootloader
→ 2nd-stage bootloader
→ your app
Upload = compile, then write ~1 MB over the USB serial link at 921 600 baud (about 10 s), then reset.
Default 4 MB flash layout (“Default 4MB with spiffs” in Tools → Partition Scheme):
boot
0x1000
table
0x8000
nvs
0x9000
ota
0xE000
app0 1.25 MB
0x10000
app1 1.25 MB
0x150000
spiffs 1.5 MB
0x290000
– Verify (✓) does step one only. Upload (→) does all of it. The first compile builds the whole core and takes 1–3 minutes; later ones take seconds.
– Two copies of the app (app0, app1) exist so a future over-the-air update can be written to one while the other runs. nvs is a small key-value store; Preferences.h writes there. spiffs is a filesystem you can put web pages in. Your board has 8 MB; the IDE default only lays out the first 4. Tools → Flash Size / Partition Scheme changes that when you need it.
Notes: What actually happens when you press Upload. First, compile: the IDE runs a GCC cross-compiler for the Xtensa architecture over your sketch, the Arduino core, and the parts of ESP-IDF you use, and links it into one binary of roughly one megabyte. That is the checkmark button, and it happens entirely on your laptop.
Second, flash: a Python tool called esptool talks to the chip over the serial link and writes that binary into the flash memory on the module, at nine hundred and twenty one thousand baud, so about ten seconds. Third, esptool resets the chip. The ROM bootloader inside the chip runs, hands over to a second-stage bootloader in flash, which reads the partition table and starts your app.
The bar at the bottom is the partition table the IDE uses by default. It lays out four megabytes; your board has eight, and you can choose a bigger scheme under Tools when a project needs it. Two slots for the app, so an over-the-air update can install into the spare slot while the current one runs. A small NVS area, a key-value store you can use from Arduino with Preferences.h to remember settings across power cycles. And a filesystem region.
Practical note: the first compile of the evening builds the entire core and takes a minute or three. After that it only rebuilds what changed.

## Slide 11
HackHardware · Getting started with the ESP32
11
Why “hold BOOT” works
CP2102N
USB-to-serial
ESP32-S3
DTR → GPIO 0
RTS → EN
Two transistors and a capacitor on EN (the RST button) make the sequence work; the BOOT button just shorts GPIO 0 to ground by hand.
EN
GPIO 0
idle
EN low: chip in reset
GPIO 0 low
EN high: chip boots, samples GPIO 0 = low → download mode
release
– At every reset the chip samples GPIO 0. High → run the program in flash. Low → wait for esptool on the serial port (download mode).
– The CP2102N's flow-control lines are wired so esptool can do this itself: DTR pulls GPIO 0 low, RTS pulses RST (EN). That is the automatic reset you normally never notice. On the other connector the chip's own USB-Serial/JTAG block does the same job with USB commands.
– When it fails you see Connecting........_____.... and then Failed to connect to ESP32-S3: Wrong boot mode detected. Hold BOOT (you are now the pull-down on GPIO 0) until Writing at 0x00010000... appears. Some boards need it every time; that is a timing quirk of their reset circuit, not a fault.
Notes: Here is the mechanism behind the single most common upload failure. At the moment of reset the chip looks at GPIO 0. If it is high, the normal case because of an internal pull-up, the chip boots your program from flash. If it is low, the chip instead sits and waits for esptool to talk to it over the serial port. That is download mode.
On a dev board, two of the serial chip's control lines, DTR and RTS, are wired through a pair of transistors to GPIO 0 and to the reset pin, which the button calls RST and the chip calls EN or CHIP_PU. esptool toggles them in a specific order, shown on the right: pull EN low to reset, pull GPIO 0 low, release EN so the chip boots and sees GPIO 0 low, then release GPIO 0. A small capacitor on EN slows its rise so the timing works out.
On some boards, with some serial drivers, the timing is off and the chip boots normally instead. esptool prints Connecting with dots and underscores, and eventually "Wrong boot mode detected". The fix is to be the transistor yourself: hold the BOOT button, which shorts GPIO 0 to ground, while esptool is connecting, and let go when you see "Writing at". Some boards need this every single time. It is a quirk of that board's reset circuit, not a fault in your code or your laptop.

## Slide 12
HackHardware · Getting started with the ESP32
12
What is running underneath your sketch
Core 0 (PRO_CPU)
Wi-Fi driver task
TCP/IP stack (lwIP)
Bluetooth controller
event loop, timers
Core 1 (APP_CPU)
loopTask — priority 1, 8 KB stack
setup() once
for(;;) loop();
your own tasks, if you create any
shared 512 KB SRAM · FreeRTOS scheduler (1 ms tick) · task watchdog
– Arduino's setup() and loop() are one FreeRTOS task, loopTask, pinned to core 1 with an 8 KB stack. The Wi-Fi driver and TCP/IP stack run on core 0. That is why Wi-Fi keeps working while your loop() is busy, and why a delay() in loop() does not drop the connection.
– delay(ms) calls vTaskDelay: it yields the core; other tasks run. millis() reads a 64-bit microsecond timer (esp_timer) and truncates to 32 bits, so it wraps after 49.7 days.
– A task watchdog resets the chip if a core is starved. If loop() spins for 5 s without yielding (for example while(1){} with no delay), you get Task watchdog got triggered and a reboot.
– Deep local arrays overflow the 8 KB stack silently → Guru Meditation Error: StackCanary watchpoint triggered. Use static or heap for big buffers.
Notes: If you are behind schedule, this slide can be skipped; the same content is in docs/CHEATSHEET.md.
People say Arduino has no operating system. On the ESP32 that is not quite true, and knowing what is there explains a lot of behaviour.
Underneath is FreeRTOS, a small real-time scheduler, with a one millisecond tick. Your setup and loop are not special: they run inside one FreeRTOS task called loopTask, created at boot with an eight kilobyte stack and pinned to core 1. Meanwhile core 0 runs the Wi-Fi driver, the TCP/IP stack, and Bluetooth. This is why Wi-Fi stays connected while your loop is doing something slow: the radio is being serviced on the other core.
Two consequences. delay does not busy-wait; it tells the scheduler to run something else for that many milliseconds. And millis comes from a 64-bit hardware timer truncated to 32 bits, so it wraps after about 49 days; the subtraction pattern we will use handles that correctly.
Two errors this explains. If your loop spins in a tight while loop for five seconds without ever yielding, a watchdog decides the core is stuck and resets the chip: "Task watchdog got triggered". And if you declare a large array as a local variable, say a four kilobyte buffer, you overflow the eight kilobyte stack and get a Guru Meditation Error mentioning the stack canary. Make big buffers static or global.

## Slide 13
HackHardware · Getting started with the ESP32
13
The shape of every sketch
#include "config.h" // LED_PIN, BOARD_NAME
// Runs once, after the bootloader hands over.
void setup() {
Serial.begin(115200);
}
// Called again as soon as it returns, forever.
void loop() {
setLed(true);
delay(500);
setLed(false);
delay(500);
}
void setLed(bool on) { // this board: RGB LED
uint8_t v = on ? 40 : 0;
rgbLedWrite(LED_PIN, v, v, v);
}
– The language is C++. You need about ten functions today; all of them are on the cheat sheet.
– There is no main() for you to write. The core provides app_main(), which starts FreeRTOS, calls setup() once, then calls loop() in a for(;;).
– config.h next to each sketch holds the pin numbers and your board's name, so a board with the LED on a different pin is a one-line change.
– A sketch folder must have the same name as the .ino inside it. That is why the repo has 01_blink/01_blink.ino.
Notes: Every sketch has this shape. setup runs once after the bootloader hands control to your program. loop is called, returns, and is called again, for as long as there is power.
The language is C++. That sounds intimidating but you will use about ten functions today, and they are all on the one-page cheat sheet in the repo.
There is no main function because the framework provides it: it starts the scheduler, creates the task we just talked about, and that task calls setup and then loop forever.
One design decision in the repo: pin numbers and your board's name live in a small file called config.h next to each sketch. If your board's LED is on 38 instead of 48, you change one line there and every task works. The small setLed function at the bottom is the only place that knows what kind of LED the board has.
And a rule of the Arduino IDE that trips people up: the sketch file must sit in a folder with the same name. That is why the repo has 01_blink slash 01_blink.ino.

## Slide 14
HackHardware · Getting started with the ESP32
14
Task 1: Blink an LED
Do this
1. File → Open tasks/01_blink/01_blink.ino
2. Tools → Board → ESP32S3 Dev Module, Tools → Port → the UART connector's port
3. Click Upload (→). If the output stops at Connecting...., hold BOOT until you see Writing at.
4. The RGB LED (white square in the middle of the board) should blink white once per second. Nothing? In config.h change LED_PIN 48 to 38, upload again.
5. In the sketch, change const unsigned long BLINK_MS = 500; to 100, upload again. Then 2000.
6. Open Serial Monitor (icon top-right), set 115200 baud. You should see the line [ESP32-1] Task 1: blink.
Check: the LED blinks at a rate you chose, and the Serial Monitor shows the start-up line.
If you finish early: make it blink SOS (three short, three long, three short); make a heartbeat (two quick blinks, pause); change the colour: rgbLedWrite(LED_PIN, 40, 0, 0) is red; ramp the brightness 0 → 40 → 0 in a loop.
Notes: Task one. Open the first sketch, check the board and port, and click Upload. The first compile takes a minute or two. When the LED starts blinking, the whole chain works: compiler, cable, driver, serial chip, bootloader, board. That is genuinely the hardest part of the day and it is now behind you.
Then make a change: set BLINK_MS to one hundred and upload again. Then two thousand. You are looking for the LED to do what you told it. Also open the Serial Monitor at one hundred fifteen thousand two hundred baud and check the start-up line appears.
If upload succeeded but nothing lights, you have the v1.1 revision of the board: open config.h, change LED_PIN from 48 to 38, upload again. If you are done early, the SOS and heartbeat variations are good practice, and since it is an RGB LED you can give it a colour: rgbLedWrite with red, green, blue values. Fifteen minutes.

## Slide 15
HackHardware · Getting started with the ESP32
15
What digitalWrite does, and why the LED needs more
// a plain LED, e.g. on a spare pin with a resistor:
pinMode(pin, OUTPUT); // enable output driver
digitalWrite(pin, HIGH); // pin -> 3.3 V
digitalWrite(pin, LOW); // pin -> 0 V
// the board's RGB LED (WS2812): one data pin,
// 24 bits per LED, each bit an 800 kHz pulse
rgbLedWrite(LED_PIN, r, g, b); // 0..255 each
– pinMode routes the pin through the GPIO matrix to the output driver. Any peripheral can be routed to almost any pin; no fixed “PWM pins” like an Arduino Uno.
– digitalWrite writes one bit in the GPIO_OUT register, about 100 ns.
– The RGB LED has its own tiny controller. It wants 24 bits (G, R, B) as pulses of 0.4 or 0.8 µs. Too fast for digitalWrite in a loop, so rgbLedWrite hands the job to the RMT peripheral, which plays the waveform from hardware.
– An external plain LED needs a resistor: 220–330 Ω at 3.3 V.
Call | Register-level effect
pinMode(p, OUTPUT) | enable output driver, route GPIO signal to pad
pinMode(p, INPUT) | disable driver, enable input buffer
pinMode(p, INPUT_PULLUP) | as INPUT, plus 45 kΩ to 3.3 V
digitalWrite(p, HIGH) | set bit p in GPIO_OUT_W1TS
digitalWrite(p, LOW) | set bit p in GPIO_OUT_W1TC
digitalRead(p) | read bit p of GPIO_IN
Notes: If you are behind schedule, this slide can be skipped; the same content is in docs/CHEATSHEET.md.
Let's name what Task 1 did, one level deeper than usual, and explain why the LED on this board needs a different function.
For a plain LED, pinMode OUTPUT does two things: it enables the output driver for that pad, and it routes the plain GPIO signal to it through something called the GPIO matrix. The matrix is a crossbar between peripherals and pads, and it is why the ESP32 has almost no fixed-function pins: any of the sixteen PWM channels, any UART, can be routed to almost any pin. That is different from an Arduino Uno, where PWM only works on marked pins.
digitalWrite sets or clears one bit in a register. It takes about a hundred nanoseconds. HIGH means the pin is driven to three point three volts, LOW to zero volts.
The LED on your board is different. It is a WS2812, the kind used in LED strips: three LEDs and a tiny controller chip in one package, with a single data input. To set a colour you send it twenty-four bits, green, red, blue, eight each, where each bit is a pulse of point four or point eight microseconds at eight hundred kilohertz. That is too fast and too precise to bit-bang with digitalWrite, so rgbLedWrite hands the waveform to a peripheral called RMT, which plays it from hardware while your code moves on. Same function drives a strip of a hundred of them.
If you connect your own plain LED to a pin, it needs a resistor, two hundred twenty to three hundred thirty ohms, or you will cook the LED and stress the pin.
The table is the same story for the functions you will use in the next task.

## Slide 16
HackHardware · Getting started with the ESP32
16
Task 2: Serial output and a button
Do this
1. Open tasks/02_serial_button/02_serial_button.ino, Upload.
2. Serial Monitor, 115200 baud. Once a second you get a line like t=12.3s temp=41.2C touch=24810 button=0 led=1
3. Press BOOT. You should see EVENT button pressed and the LED stops or starts blinking.
4. Touch the header pin labelled 4 (left side, near RST) with a finger. The touch= value jumps up.
5. Change REPORT_MS to 250 and upload. Then look at loop(): there is no delay() in it.
6. Tools → Serial Plotter graphs the numbers. Touch the pin and watch.
Check: pressing BOOT prints a new line in the Serial Monitor.
If you finish early: count presses and print the total; make the blink rate change with each press; print ESP.getFreeHeap() in the status line and watch it.
Notes: Task two adds the two things every real project needs: a way to see what the chip is thinking, and a way to tell it something.
Upload the sketch and open the Serial Monitor at one hundred fifteen thousand two hundred. Once a second you get a status line: uptime, the chip's internal temperature, a touch reading, the button state, and the LED state.
Press BOOT. You should see "EVENT button pressed" and the LED toggles between blinking and off. Touch the header pin labelled four with a finger and watch the touch value jump up; the chip has capacitive touch sensing built in. On this chip touching makes the number bigger; on the original ESP32 it was the other way round, so old tutorials will say it drops.
Then look at the code and notice there is no delay anywhere in loop. That is deliberate and we will explain it on the next slides. If you finish early, the Serial Plotter under Tools graphs whatever numbers you print, which is a nice way to see the touch sensor react.

## Slide 17
HackHardware · Getting started with the ESP32
17
Serial: the console you do not have
– The chip has no screen. Serial is UART0 on GPIO 43 (TX) and 44 (RX), which the CP2102N behind the UART connector turns into a COM port. On the other connector Serial only works with *USB CDC On Boot* enabled.
– Both ends must agree on the speed. 115200 baud = 115 200 bits/s ≈ 11 500 characters per second. A mismatch shows as garbage like ⸮⸮⸮x⸮.
– The chip's ROM prints its own boot messages at 115200 before your code runs. That is what rst:0x1 (POWERON) and ESP-ROM:esp32s3-20210327 are. Not an error.
– Opening the Serial Monitor toggles DTR, which resets the board. So you always see the start-up line, and any state is lost.
– Serial.print writes to a 128-byte buffer that the UART drains at 115200. Printing more than ~11 KB/s blocks loop(); printing every loop iteration is the classic mistake.
– Serial.printf("t=%.1f temp=%.1f\n", t, c); works on ESP32 and is easier to read than chained prints.
Serial.begin(115200);
// once per second:
Serial.print("t=");
Serial.print(millis() / 1000.0, 1);
Serial.print("s temp=");
Serial.print(temperatureRead(), 1);
Serial.println("C");
// same thing:
Serial.printf("t=%.1fs temp=%.1fC\n",
millis() / 1000.0, temperatureRead());
Typical ROM boot log you will see before your own output:
ESP-ROM:esp32s3-20210327
rst:0x1 (POWERON),boot:0x8 (SPI_FAST_FLASH_BOOT)
SPIWP:0xee
mode:DIO, clock div:1
load:0x3fce2820,len:0x118c
entry 0x403c8b08
Notes: The chip has no screen, so Serial is how you see what it is doing. Technically it is UART zero, a hardware serial port on pins 43 and 44, and the CP2102N chip behind the UART connector converts that to USB so your laptop sees a serial port. That is why the other connector shows nothing: it bypasses that chip.
Both sides have to agree on speed. We use one hundred fifteen thousand two hundred baud everywhere. If the monitor is set to nine thousand six hundred you get garbage characters instead of text. That is the first thing to check when Serial output looks wrong.
Two things that confuse beginners. First, before your code runs, the chip's own ROM prints a few lines at 115200: ESP-ROM, rst colon, boot colon, load, entry. That is the bootloader talking; it is not an error. You will see it every reset. Second, opening the Serial Monitor resets the board, because the IDE toggles the DTR line, the same line used for programming. So you always see the start-up message, and whatever state the board was in is gone.
A performance note: Serial.print writes into a small buffer that drains at eleven thousand characters a second. If you print on every pass through loop, you will block waiting for the buffer. Print on a timer, like the sketch does. And Serial.printf works on ESP32 and reads better than a chain of prints.

## Slide 18
HackHardware · Getting started with the ESP32
18
Reading a button: pull-ups and bounce
3.3 V
45 kΩ pull-up inside the chip,
enabled by INPUT_PULLUP
GPIO 0 → digitalRead()
BOOT button
GND
Button | Pin voltage | digitalRead
released | 3.3 V through the resistor | HIGH (1)
pressed | 0 V, shorted to ground | LOW (0)
nothing connected, no pull-up | floating — picks up noise | random
– An unconnected input floats: it reads whatever charge is on the wire, so it flickers between 0 and 1. The pull-up gives it a defined level when the button is open. Pressed therefore reads LOW. Backwards, but standard.
– A mechanical contact bounces for 1–10 ms when it closes, producing several edges. Read the pin every loop, and only accept a new state after it has been stable for ~30 ms.
– React to the edge (state changed) rather than the level (is pressed), or one press toggles the LED thousands of times while your finger is down.
Notes: Reading a button sounds trivial, and there are two traps in it.
First, an input pin with nothing connected is floating: it reads whatever stray charge is on the wire, and flickers between zero and one. To get a clean reading, you need a resistor that gently holds the pin at a known level when the button is not pressed. The ESP32 has one built into every pin, about forty-five kilohms, and INPUT_PULLUP turns it on. The BOOT button is wired between GPIO 0 and ground, so pressing it drags the pin to zero volts. Pressed equals LOW. That feels backwards, and now you know why it is that way.
Second, a mechanical switch does not close cleanly. For a few milliseconds the contacts bounce, and the pin sees several transitions. If you count edges you count several presses. The fix in the sketch is simple: remember when the reading last changed, and only accept the new state once it has held for thirty milliseconds.
And a third habit: react to the moment of change, not to the state. If you toggle the LED whenever the pin is LOW, it toggles thousands of times while your finger is down. The sketch compares the current debounced state to the previous one and acts only on the transition.

## Slide 19
HackHardware · Getting started with the ESP32
19
Timing without delay()
Blocking
void loop() {
digitalWrite(LED_PIN, HIGH);
delay(500); // loop() is stuck here
digitalWrite(LED_PIN, LOW);
delay(500); // presses now are missed
}
Non-blocking
unsigned long lastBlink = 0;
void loop() {
unsigned long now = millis();
if (now - lastBlink >= BLINK_MS) {
lastBlink = now;
setLed(!ledOn);
}
checkButton(); // ~100 000 calls/s
server.handleClient(); // Task 4
}
– delay() lets other FreeRTOS tasks run (Wi-Fi is fine), but nothing else in your loop() runs. In Task 4 the web server is polled from loop(), so a delay(500) means the page takes up to 500 ms to respond.
– Write now - last >= interval, never now >= last + interval. Unsigned subtraction gives the right answer across the 32-bit wrap at 49.7 days; addition does not.
– Need real parallelism? Create another FreeRTOS task: xTaskCreatePinnedToCore(fn, "name", 4096, NULL, 1, NULL, 1);. That is what the Wi-Fi driver does.
Notes: This is the most important habit in the workshop.
delay stops your loop for that long. Because of what we saw about FreeRTOS, the Wi-Fi driver on the other core keeps running, so the connection survives. But nothing else in your loop runs: the button is not read, and in Task 4 the web server is not serviced, so your phone waits.
The alternative on the right: keep a note of when you last did something, and each time through loop, check whether enough time has passed. If yes, do it and update the note. If not, move on. loop runs about a hundred thousand times a second, so every job is checked constantly and nothing is missed. Every sketch from Task 2 onward is written this way.
One detail that matters: write now minus last, greater or equal to interval. Unsigned subtraction gives the right answer even when millis wraps around after forty-nine days. Writing now greater than last plus interval breaks at the wrap.
And if you genuinely need two things to run at the same time, you can create a second FreeRTOS task and pin it to a core. That is beyond today, but the one-liner is on the slide and it is exactly what the Wi-Fi driver itself does.

## Slide 20
HackHardware · Getting started with the ESP32
20
The sensors already on the chip
Call | What it measures | How it works | What to expect
touchRead(T4) | capacitance on GPIO 4 | Charges and discharges the pad and measures how long it takes. More capacitance (a finger) → a larger count on the S3 (smaller on the original ESP32). | ≈ 20 000–30 000 untouched, 40 000+ touched on a bare header pin. Very board- and humidity-dependent. Fourteen pads: T1–T14 on GPIO 1–14.
temperatureRead() | die temperature, °C | Internal sensor next to the CPU, read through ADC. | Reads 40–60 °C on a warm chip; ±few °C at best; drifts with Wi-Fi load. Good for trends, not for room temperature.
analogRead(pin) | voltage on an ADC pin | 12-bit SAR ADC, 0–4095. Default 12 dB attenuation, usable range ≈ 0–3100 mV. Uses factory calibration in core 3.x. | Nonlinear near the top. Noisy: average 8–16 samples. ADC1 = GPIO 1–10; ADC2 (11–20) is unreliable with Wi-Fi on.
analogWrite(pin, 0–255) | (output) PWM duty | LEDC peripheral: 8 channels, 1 kHz, 8-bit by default in core 3.x. ledcAttach(pin, freq, bits) for full control. | Dims a plain LED, drives servos (50 Hz) and buzzers. Does not work on the RGB LED; set its brightness through rgbLedWrite values instead.
rgbLedWrite(pin, r, g, b) | (output) RGB LED colour | Sends 24 bits to a WS2812 through the RMT peripheral; works for the onboard LED and for LED strips (rgbLedWrite for one, a library like FastLED for many). | Full brightness is blinding; 20–60 is comfortable. Order is r, g, b.
Task 2 prints touch and temperature; Task 4 shows them on a web page. analogRead needs a potentiometer or a light sensor; helpers have a few if you want to try.
Notes: If you are behind schedule, this slide can be skipped; the same content is in docs/CHEATSHEET.md.
The status line in Task 2 uses two sensors that are already inside the chip, and it is worth knowing what they really measure.
touchRead: each of the fourteen touch pads works by repeatedly charging and discharging the pin and measuring the time that takes. A finger adds capacitance, which slows the charging, and on this chip the number reported goes up. Untouched you get something around twenty-five thousand, touched forty thousand or more. The original ESP32 reported it the other way round, so old tutorials will say the value drops. The absolute values depend on the board, the wire, and how humid the room is, so any code that uses touch needs a threshold you tune by looking at the numbers.
temperatureRead is the die temperature, next to the CPU. It reads forty to sixty degrees on a running chip, it drifts with load, and it is accurate to a few degrees at best. It is a trend indicator, not a room thermometer. For real temperature you add a two-dollar sensor.
analogRead is a twelve-bit converter giving zero to 4095. With the default attenuation the usable range is roughly zero to three point one volts, it is nonlinear near the top, and it is noisy, so average several samples. Use pins one to ten; ADC2 on eleven to twenty is unreliable once Wi-Fi is on.
analogWrite is the output side: pulse width modulation through the LEDC peripheral. The pin switches on and off a thousand times a second and the duty cycle sets the apparent brightness of a plain LED, or the position of a servo. It does nothing useful on the RGB LED, which has its own controller; there you set brightness through the colour values in rgbLedWrite.

## Slide 21
HackHardware · Getting started with the ESP32
21
Task 3: Turn on Wi-Fi
Do this
1. Open tasks/03_wifi/config.h. Set BOARD_NAME to something unique and short, e.g. "ESP32-felipe". This becomes your network name.
2. Open 03_wifi.ino, Upload, open Serial Monitor.
3. First a table: every network in the room with channel, signal strength (RSSI) and security. Find the campus Wi-Fi and see its channel.
4. Then: AP started SSID: ESP32-felipe IP: 192.168.4.1
5. On your phone, open Wi-Fi settings, join ESP32-<your name>, password hackhardware. Accept “no internet connection”.
6. The LED blinks faster while a device is connected. Serial prints client connected with the phone's MAC address.
Check: your phone is connected to your board's network.
If you finish early: set USE_STATION_MODE 1 and put your phone's hotspot name and password in config.h; the board joins it and prints the IP it was given. Or print only the strongest network and its RSSI, updating every 2 s.
Notes: Task three turns the radio on. First, in config.h, give your board a name. It becomes the Wi-Fi network name, and in a minute this room will have forty of them, so make it something you recognise. Keep it short.
Upload and watch the Serial Monitor. The first thing the sketch does is scan: every network within range, its channel, signal strength in dBm, and security type. Find the campus Wi-Fi in the list. Minus forty dBm is excellent, minus seventy is fine, minus ninety is barely there. The scan needs no password and always works, so if you see the table, the radio is alive.
Then the board starts its own access point, named after your board, and prints its address, one nine two dot one six eight dot four dot one. Open Wi-Fi settings on your phone and join it, password hackhardware. Your phone will complain that there is no internet. That is correct; stay connected. The LED speeds up when a device is connected, and Serial prints the phone's MAC address.
If you finish early, the station mode option makes the board join your phone's hotspot instead, which is how you would do it at home.

## Slide 22
HackHardware · Getting started with the ESP32
22
Wi-Fi on the ESP32-S3
Station (STA): the board joins a network
phone /
laptop
router or
hotspot
ESP32
Needs the network name and password in code. Gets an address from the router by DHCP. Campus Wi-Fi usually uses WPA2-Enterprise (username + password), which the WiFi library cannot join in one line, and isolates clients from each other — so your phone could not reach the board anyway.
Access point (AP): the board is the network
phone /
laptop
ESP32 runs the AP + DHCP server
192.168.4.1
The board creates its own 2.4 GHz network and hands out addresses 192.168.4.2 onward. Default limit is 4 connected devices (up to 10 with WiFi.softAP(ssid, pass, ch, hidden, max)). Works in any room with no infrastructure. Your phone will warn “no internet” — that is expected.
RSSI | Meaning
−30 to −50 dBm | excellent, same desk
−50 to −67 dBm | good, same room
−67 to −80 dBm | usable, slow
below −85 dBm | drops out
Band | 2.4 GHz only. A phone on a 5 GHz-only network will not see the board.
Standards | 802.11 b/g/n, up to 150 Mbps on air; ~20 Mbps TCP in practice
Stack | lwIP TCP/IP, DHCP client and server, DNS, mDNS (ESPmDNS.h)
Modes | WIFI_STA, WIFI_AP, WIFI_AP_STA (both at once, same channel)
Notes: Two roles a Wi-Fi radio can play. Station is what your laptop does: join a network someone else runs, get an address from their router. Access point is what the router does: create the network, hand out addresses. The ESP32 can do either, or both at the same time.
Today we default to access point mode, and the reason is practical. Campus Wi-Fi typically uses WPA2-Enterprise, which needs a username and certificate handling that the basic WiFi library does not do in one line, and it isolates clients from each other, so even if the board joined, your phone could not reach it. Making the board its own network sidesteps all of that: the phone connects directly, the board runs a small DHCP server, and its own address is always 192.168.4.1. By default four devices can connect at once.
Some numbers to keep in mind. The radio is 2.4 gigahertz only, so a phone locked to a 5 gigahertz network will never see the board. RSSI, the signal strength, is in dBm: minus fifty is great, minus seventy is fine, below minus eighty-five it drops. The TCP/IP stack is lwIP, the same one used in a lot of embedded products, with DHCP and DNS and multicast DNS, which lets you reach the board at a dot-local name instead of an IP.

## Slide 23
HackHardware · Getting started with the ESP32
23
Task 4: A web page served by the board
Do this
1. Open tasks/04_web_dashboard/04_web_dashboard.ino. Check BOARD_NAME in its config.h. Upload.
2. On your phone, join ESP32-<name> again. If the page will not load, turn off mobile data; the phone is routing around the “no internet” network.
3. In the browser go to http://192.168.4.1 (http, not https). You get a status page that updates every second.
4. Tap LED on / off. The LED on the desk changes. Press BOOT on the board; the page notices.
5. Open http://192.168.4.1/api/status. That is the raw JSON the page is reading.
6. Find the two // ---- add your own ... comments in the sketch. Add a field, upload, reload.
Check: you can switch the LED from your phone.
If you finish early: add a /api/blink?n=3 route that blinks n times (set a counter, let loop() do the blinking); show ESP.getFreeHeap() on the page; change the page's colours in page.h.
Notes: Task four is the longest, about thirty minutes. Upload the dashboard sketch, join your board's network again on your phone, and open one nine two dot one six eight dot four dot one in a browser. You get a plain status page: your board's name, uptime, temperature, touch, button, LED state, and two buttons.
Tap LED on. The LED on your desk turns on. That is the moment where it clicks for most people: a phone controlling hardware you programmed, with no cloud, no app, no account.
Two snags. If the page will not load, your phone has probably decided the board's network is useless because it has no internet, and is sending requests over mobile data. Turn mobile data off. And type http, not https; the board does not do TLS.
Then look under the hood: open slash api slash status in the browser and you see the JSON the page is polling. Then find the two "add your own" comments in the sketch and add a field. Upload, reload, and it appears. That is the pattern for everything you will ever put on one of these pages.

## Slide 24
HackHardware · Getting started with the ESP32
24
HTTP on a microcontroller
#include <WebServer.h>
WebServer server(80);
void handleStatus() {
String j = "{\"uptime_s\":" + String(millis()/1000);
j += ",\"temp_c\":" + String(temperatureRead(), 1);
j += ",\"led\":" + String(ledOn ? 1 : 0) + "}";
server.send(200, "application/json", j);
}
void setup() {
// ... Wi-Fi AP up ...
server.on("/", handlePage);
server.on("/api/status", handleStatus);
server.on("/api/led", handleLed);
server.begin();
}
void loop() {
server.handleClient();
updateLed();
}
– A request is text: GET /api/led?state=on HTTP/1.1. The server matches the path to a function you registered with server.on(), the function builds a reply, server.send() writes status code, content type and body.
– WebServer is single-threaded and polled: handleClient() checks for a waiting connection each time loop() calls it. No delay() in loop(), or the page stalls.
– Query parameters: server.arg("state"), server.hasArg("n").
– JSON is built by hand here, with a few String concatenations. For anything bigger, the ArduinoJson library.
– The page HTML lives in page.h as a raw string literal in flash (PROGMEM), ~8 KB. One page, no external files, so it works with no internet.
– Throughput: roughly 20–50 small requests per second. Plenty for one phone polling once a second.
Notes: What a web server is, stripped to the bone. The phone sends a request, which is a line of text: GET, a path, and a protocol version, followed by some headers. The server matches the path to a function. The function builds a reply and sends it back with a status code and a content type. That is everything.
The WebServer library that ships with the ESP32 core does exactly that. server.on registers a path and the function to call. server.begin starts listening on port 80. And server.handleClient, called from loop, checks whether a connection is waiting and services it. That last point matters: it is polled, not threaded. If your loop is stuck in a delay, no one is answering the phone.
Query parameters after the question mark come out with server.arg. For the reply we use JSON, a text format that the JavaScript in your phone's browser parses natively. In this sketch it is built by hand with string concatenation because the fields are few. For anything bigger you would use the ArduinoJson library.
The page itself, the HTML and JavaScript, is stored as one big string in flash and sent when the browser asks for slash. It is self-contained, with no external files, so it works with no internet at all. Throughput is a few dozen small requests per second, which is plenty for a phone asking once a second.

## Slide 25
HackHardware · Getting started with the ESP32
25
How the page and the board talk
Browser on your phone
page HTML + JavaScript
setInterval(…, 1000):
fetch('/api/status')
→ update the numbers
ESP32 at 192.168.4.1:80
loop():
server.handleClient()
→ match path to handler
→ read sensors, build JSON
→ server.send(200, …)
GET /api/status HTTP/1.1
200 OK {"uptime_s":42,"temp_c":41.2,"led":1}
one round trip ≈ 5–30 ms on the local link
// in page.h: the JavaScript the browser runs
setInterval(async () => {
const s = await (await fetch('/api/status')).json();
document.getElementById('temp').textContent
= s.temp_c.toFixed(1) + ' °C';
document.getElementById('led').textContent
= s.led ? 'on' : 'off';
}, 1000);
// a button: onclick="fetch('/api/led?state=on')"
The board never pushes anything; the browser asks once a second. That is the simplest possible “live” page. WebSockets or Server-Sent Events are the next step if you need lower latency.
Notes: Here is the whole system in one picture. The board serves one HTML page. That page contains a few lines of JavaScript. Once a second, a timer fires, fetch asks the board for slash api slash status, the board reads its sensors, builds a JSON string, and replies. The JavaScript puts the numbers into the page. Ask, answer, redraw, forever. That is what makes it feel live, and it is about eight lines of code.
Commands go the same way in the other direction: a button's onclick calls fetch on slash api slash led with state equals on. The handler flips the pin and replies.
Notice the board never pushes anything. Polling once a second is the simplest way to build a live page, and for one phone and one board it is completely adequate. If you ever need lower latency, or many clients, the next step is WebSockets or Server-Sent Events, and the ESP32 does both. But start here.

## Slide 26
HackHardware · Getting started with the ESP32
26
Extending the dashboard
Add a field to the JSON
// handleStatus(), at the marked comment:
j += ",\"heap_free\":"
+ String(ESP.getFreeHeap());
j += ",\"rssi\":" + String(WiFi.RSSI());
Show it on the page (page.h)
<div>Free heap:
<span id="heap">–</span> bytes</div>
// in the setInterval callback:
document.getElementById('heap')
.textContent = s.heap_free;
Add a command
int blinksLeft = 0;
// GET /api/blink?n=3
void handleBlink() {
blinksLeft = server.arg("n").toInt();
server.send(200, "application/json",
"{\"ok\":true}");
}
// in setup():
// server.on("/api/blink", handleBlink);
// in loop():
// if (blinksLeft > 0) blinkWithMillis();
Handlers must return immediately. Set a variable; let loop() do the slow thing. Test a new route by typing its URL in the browser before wiring up a button.
Notes: Three ways to make the dashboard yours, and they are the same three moves you will use in any project on this chip.
Adding a field: find the marked comment in handleStatus and append one more name and value to the JSON string. Free heap is a good one; it shows you how much memory your program has left and whether it is leaking. Then add a span to the page and one line in the JavaScript to fill it.
Adding a command: register another route in setup, read a parameter with server.arg, and reply. The important habit is on the slide: the handler sets a variable and returns immediately. It does not blink the LED itself with delays, because that would stall the server. loop sees the counter and does the blinking with millis, the way we learned in Task 2.
And a debugging habit: type your new route into the phone's browser before you wire up a button. If the JSON looks right there, the remaining work is HTML.

## Slide 27
HackHardware · Getting started with the ESP32
27
Task 5: Messages between boards (optional)
Do this
1. Open tasks/05_esp_now/05_esp_now.ino (same BOARD_NAME as before), Upload.
2. Serial prints your board's MAC address and, every 2 s, a table of other boards it can hear: name, age, temperature, LED state.
3. Reload http://192.168.4.1. A new section, Boards nearby, lists the same table.
4. Walk to another table. Watch boards appear and drop off after 10 s without a packet.
5. Look at struct Message in the sketch: 24 bytes. That is the whole packet payload.
Check: another board's name appears in your list.
If you finish early: send a command instead of a status: press BOOT on your board and make a neighbour's LED toggle; add the sender's RSSI (info->rx_ctrl->rssi) to the table.
Notes: Task five is for people who are ahead, and it is the most interesting one technically. ESP-NOW is Espressif's protocol for sending small packets directly between boards, with no router, no IP addresses, no connection. Like walkie-talkies.
The sketch broadcasts a small struct, your board name, uptime, temperature, and LED state, every two seconds, to the broadcast address. Every board in range that hears it adds the sender to a table; entries that go ten seconds without a packet are dropped. The table prints to Serial and shows up as a new section on the web page.
Walk around the room with your board and watch names appear and disappear. Then look at the struct in the code: twenty-four bytes. That is the entire payload. If you finish, try turning it into a command: press your button and make a neighbour's LED toggle.

## Slide 28
HackHardware · Getting started with the ESP32
28
ESP-NOW: what is on the air
802.11 MAC header
24 B
Category
1 B (127 = vendor)
Org. ID
3 B
Random
4 B
Element ID
1 B (221)
Length
1 B
OUI
3 B
Type
1 B
Ver.
1 B
Body — your struct
0–250 B
A vendor-specific action frame: a management frame any 802.11 radio can receive without joining a network. Sent at 1 Mbps by default; a full 250-byte packet takes about 2.5 ms of air time.
– No association, no DHCP, no TCP: a board sends a frame to a MAC address (or FF:FF:FF:FF:FF:FF for everyone) and any ESP32 listening on that channel receives it. Latency is a few ms.
– Payload up to 250 bytes in v1; the S3 on core 3.x also speaks ESP-NOW v2 with up to 1470 bytes between v2 boards. Optional per-peer AES encryption; up to 20 peers.
– Coexists with the access point: WiFi.mode(WIFI_AP_STA) and fix the AP channel so both radios agree. The sketch uses channel 1.
struct Message {
char name[12];
uint32_t uptime_s;
float temp_c;
uint8_t led;
}; // 24 bytes
void onReceive(const esp_now_recv_info_t *info,
const uint8_t *data, int len) {
Message m; memcpy(&m, data, sizeof m);
addPeer(m, info->src_addr); // keep it short
}
esp_now_init();
esp_now_register_recv_cb(onReceive);
esp_now_send(bcast, (uint8_t*)&me, sizeof me);
Notes: What ESP-NOW actually puts on the air. Wi-Fi has a class of packets called management frames that a radio can receive without being joined to any network; that is how your phone sees network names before connecting. Espressif uses one of those, a vendor-specific action frame, and puts your data in the body. Up to 250 bytes in the original version.
Because there is no association and no TCP, it is fast: a few milliseconds from send to receive callback. It works between any ESP32s on the same channel, in range, with nothing else in between. You can optionally encrypt per peer.
The one constraint that catches people: the radio has a single channel at a time. If your access point is on channel 6 and a neighbour's board is on channel 1, they cannot hear each other. The sketch pins everything to channel 1 and runs the radio in AP plus station mode so the access point and ESP-NOW share it.
Note the receive callback runs inside the Wi-Fi driver's task on core 0. Keep it short: copy the data into your table and return. Printing to Serial inside it works but is bad form; doing anything slow there will stall the radio.

## Slide 29
HackHardware · Getting started with the ESP32
29
Time left? Pick one
Shorter
– Blink your board name in Morse code
– Reaction-time game: LED comes on at a random moment, press BOOT, print your time
– Touch pin controls the LED's brightness or colour with rgbLedWrite
– Reach the board at http://<name>.local with ESPmDNS
– Show the strongest Wi-Fi network live in the Serial Monitor
Longer
– /api/blink?n= route plus a button on the page; or /api/color?r=&g=&b= with an <input type="color">
– Remember the board name across reboots with Preferences.h (NVS)
– Temperature graph on the page with <canvas>
– Deep sleep for 10 s, wake, print the boot count kept in RTC_DATA_ATTR memory
– Rate-limit your API: reject more than 5 requests/s per client
– Two boards: press BOOT on one, LED toggles on the other (ESP-NOW)
Each one is in CHALLENGES.md with a hint and a “done when”. Ask a helper if you are stuck for more than a few minutes.
Notes: If you have time left, choose one of these. The short ones are twenty-minute wins with the code you already have. The longer ones each introduce something we did not cover: persistent storage with Preferences, deep sleep and the RTC memory that survives it, a drawing on the page, a bit of security.
Each one is written up in the challenges file with a hint pointing at the exact function and a definition of done. Pick whatever sounds fun rather than whatever sounds important. Helpers are around. In about fifteen minutes we regroup and a few people show what they built.

## Slide 30
HackHardware · Getting started with the ESP32
30
What we skipped, and where to go next
Topic | One line
Interrupts | attachInterrupt(pin, isr, FALLING): react to a pin in microseconds instead of polling
FreeRTOS tasks | xTaskCreatePinnedToCore: real parallelism, queues, semaphores
I²C / SPI sensors | Wire.h: a BME280 (temp, humidity, pressure) or MPU6050 (motion) costs $2–4
Deep sleep | esp_deep_sleep(us), wake on timer, touch or pin; months on batteries
OTA updates | ArduinoOTA or Update.h: reflash over Wi-Fi into the spare app slot
MQTT | PubSubClient: publish sensor data to a broker; Home Assistant picks it up
Bluetooth | BLE server in BLEDevice.h; a phone app or Web Bluetooth talks to it
Filesystem | LittleFS: store web pages and logs in the spiffs partition
– PlatformIO in VS Code: same code, real project structure, library versioning, unit tests.
– ESP-IDF directly: everything Arduino hides: menuconfig, components, the full FreeRTOS API. Arduino can even be a component inside an IDF project.
– Other chips: the original ESP32 (cheaper, Bluetooth Classic, most tutorials), C6 (RISC-V, Wi-Fi 6, Zigbee), P4 (no radio, big CPU). Same Arduino core, different pin numbers.
– Read the code you ran today. Each sketch is commented for exactly this.
Notes: We covered pins, serial, timing, Wi-Fi, HTTP and ESP-NOW. Here is what we deliberately skipped, in one line each, so you know the names to search for.
Interrupts, to react to a pin within microseconds rather than checking it in loop. FreeRTOS tasks, for real parallelism. I2C and SPI sensors, which is where projects get real: a temperature, humidity and pressure sensor costs a couple of dollars and speaks I2C on pins 21 and 22. Deep sleep for battery projects. Over-the-air updates into that spare app slot we saw in the partition table. MQTT to publish data to a broker and have Home Assistant pick it up. Bluetooth. And a filesystem for storing pages and logs.
On tooling: PlatformIO in VS Code is where most people go after Arduino IDE, same code but with proper project structure and library versions. And ESP-IDF is Espressif's own framework, with everything Arduino hides; you can even embed Arduino as a component in it.
The most useful thing you can do this week is read the five sketches you ran today. They are commented for exactly that.

## Slide 31
HackHardware · Getting started with the ESP32
31
Buying a board
Look for | Why
ESP32-S3-DevKitC-1 (N8R8 or N16R8), what you used today | Espressif's own board, both USB modes, PSRAM. About $10–15. Clones with the same name and layout exist for less; most copy the GPIO 48 revision.
"ESP32 DevKit V1" / "ESP32-WROOM-32" (the original chip) | The board most tutorials are written for. $4–8. Plain LED on GPIO 2, Bluetooth Classic, no native USB. Today's code runs on it with three lines changed in config.h.
ESP32-C3 / C6 boards | Smallest and cheapest ($2–5), RISC-V, single core. Fine for sensors; slower for web serving.
Serial chip: CP2102 or CH340 | Both fine. CP2102 (what your board has) has fewer driver problems on Windows.
USB-C vs micro-USB | Check before buying a cable. Either way, a data cable.
Also useful | Breadboard, jumper wires, a few LEDs + 220 Ω resistors, one I²C sensor (BME280, MPU6050), a short WS2812 strip (same rgbLedWrite idea), a USB power bank.
Sold on every large marketplace and at electronics shops. The club can organise a group order; ask at the end.
Notes: If you want to keep going, get your own board. The simplest choice is the one in front of you: an ESP32-S3-DevKitC-1, ten to fifteen dollars from Espressif's distributors, or less for a clone with the same layout. Everything from today runs on it unchanged.
The original ESP32 DevKit is the cheaper sibling and it is what most tutorials online are written for; four to eight dollars. It has a plain LED, Bluetooth Classic, and no native USB. Today's code runs on it with three lines changed in config.h; the comments in that file say which.
The C3 and C6 are tiny and cheap, single-core RISC-V, great for sensors, a bit slower at serving web pages.
Buy a data cable at the same time and check whether the board is USB-C or micro-USB. A breadboard, jumper wires, a handful of LEDs and resistors, and one I2C sensor turn the board into a kit; a short strip of WS2812 LEDs is a fun next step because you already know how to drive one. The club may do a group order; ask us.

## Slide 32
HackHardware · Getting started with the ESP32
32
Wrap-up
Show what you built
– Whose page has the most fields? Whose board list is longest?
– What broke, and what fixed it? Those are the useful stories.
What you now know
– How code gets onto the chip, and what to do when it does not
– Which pins to use and which to avoid, and which USB connector
– Outputs, inputs, debouncing, timing without delay()
– Wi-Fi as station and as access point
– Serving a page and a JSON API from a microcontroller
– Sending packets directly between boards
Links
– Code, setup guide, troubleshooting, challenges: github.com/galileoisonline/esp32-workshop
– HackHardware: [CLUB DISCORD/LINK]
– Feedback (one minute): [FEEDBACK LINK]
– Next session: [DATE / TOPIC]
Keep the board if we said you could. It is yours; the code is on the repo.
Notes: Let's finish with a quick round of show and tell. Who added the most fields to their page? Whose boards-nearby list is longest? And the most useful question: what broke for you, and what fixed it? Those stories help the next person more than anything I said.
Everything from today is in the repository: the code, the setup guide, the troubleshooting page, and the challenges. Join the club channel; that is where the next sessions and group board orders get organised. Please fill in the feedback form before you leave; it takes a minute and decides what we run next.
Thank you for coming, thank you to the helpers, and keep hacking on the board.